## Slide 1
DATASET AND DSP CONTRACT
128,400
WINDOWS
8
SIGNAL CLASSES
6
SNR BINS · −10 TO +10 dB
WHERE THE DATA COMES FROM
THE FORMAT CONTRACT
01
RADIOML 2018.01A
Civilian modulations, third-party dataset
BPSK
QPSK
16QAM
64QAM
02
RADCHAR
Every standalone radar window is real third-party data
LFM RADAR
03
OUR OWN GENERATORS
No public raw-IQ dataset covers these three
FHSS
JAMMING
NOISE FLOOR
SAMPLE RATE
3.2 MHz
WINDOW LENGTH
512 samples = 160 µs
REPRESENTATION
2 × 512 (I and Q)
NORMALISATION
zero mean, unit variance
Why normalisation matters: raw window power varies by 18 dB across the SNR range, and the slope differs per class — otherwise the model learns loudness, not signal.
Notes: Our dataset is 128,400 windows across eight classes and six SNR bins, from minus ten to plus ten decibels. Civilian modulations come from RadioML. Radar comes from RadChar - every standalone radar window is real third-party data. FHSS, jamming and the empty channel we generate ourselves, because no public raw-IQ dataset covers them. Everything is forced through one DSP contract: 512 samples at 3.2 megahertz - a 160-microsecond window - normalised to zero mean and unit variance. Raw window power varies by eighteen decibels across our SNR range, and the slope differs per class.